## Slide 1: – Slides adapted from – Introduction to Computer Networks
Aditya Akella
Lecture 5 - Encoding and Data Link Basics

## Slide 2: Signals, Data and Packets
Analog Signal
“Digital” Signal
Bit Stream
0 0 1 0 1 1 1 0 0 0 1
Packets
0100010101011100101010101011101110000001111010101110101010101101011010111001
Header/Body
Header/Body
Header/Body
Receiver
Sender
Packet
Transmission

## Slide 3: Binary data to Signals
Modulation: changing attributes of signal to effect information transmissions
Encoding
  How to convert bits to “digital” signals
  Very complex, actually
  Error recovery, clock recovery,…

## Slide 4: Modulation Schemes
Data
Amplitude Modulation
Frequency Modulation
Phase Modulation

## Slide 5: Why Do We Need Encoding?
Meet certain electrical constraints.
  Receiver needs enough “transitions” to keep track of the transmit clock
  Avoid receiver saturation
Create control symbols, besides regular data symbols.
  E.g. start or end of frame, escape, ...
  Important in packet switching
Error detection or error corrections.
  Some codes are illegal so receiver can detect certain classes of errors
  Minor errors can be corrected by having multiple adjacent signals mapped to the same data symbol

## Slide 6: Encoding
Use two signals, high and low, to encode 0 and 1.
Transmission is synchronous, i.e., a clock is used to sample the signal.
  In general, the duration of one bit is equal to one or two clock ticks
  Receiver’s clock must be synchronized with the sender’s clock
Encoding can be done one bit at a time or in blocks of, e.g., 4 or 8 bits.

## Slide 7: Non-Return to Zero (NRZ)
1 -> high signal; 0 -> low signal
Long sequences of 1’s or 0’s can cause problems:
  Hard to recover clock
  Difficult to interpret 0’s and 1’s
V
0
.85
-.85
0
0
0
1
1
0
1
0
1

## Slide 8: Non-Return to Zero Inverted (NRZI)
1 -> make transition; 0 -> signal stays the same
Solves the problem for long sequences of 1’s, but not for 0’s.
V
0
.85
-.85
0
0
0
1
1
0
1
0
1

## Slide 9: Ethernet Manchester Encoding
Positive transition for 0, negative for 1
XOR of NRZ with clock
Transition every cycle communicates clock (but need 2 transition times per bit)
Problem: doubles the rate at which signal transitions are made
  Less efficient
  Receiver has half the time to detect the pulse
V
0
.85
-.85
0
1
1
0
.1s

## Slide 10: 4B/5B Encoding
Data coded as symbols of 5 line bits => 4 data bits, so 100 Mbps uses 125 MHz.
  Uses less frequency space than Manchester encoding
Each valid symbol has no more than one leading zero and no more than two trailing zeros
  At least two 1s  Get dense transitions
Uses NRZI to encode the 5 code bits
  What happens if there are consecutive 1s?

## Slide 11: 4B/5B Encoding
0000
0001
0010
0011
0100
0101
0110
0111
11110
01001
10100
10101
01010
01011
01110
01111
Data
Code
1000
1001
1010
1011
1100
1101
1110
1111
10010
10011
10110
10111
11010
11011
11100
11101
Data
Code
16 data symbols, 8 control symbols
  Control symbols: idle, begin frame, etc.
  Remaining 8 are invalid

## Slide 12: Other Encodings
8B/10B: Fiber Channel and Gigabit Ethernet
  DC balance
64B/66B: 10 Gbit Ethernet
B8ZS: T1 signaling (bit stuffing)

## Slide 13: Datalink Protocol Functions
Framing: encapsulating a network layer
  Add header, mark and detect frame boundaries, …
Error control: error detection and correction to deal with bit errors.
  May also include other reliability support, e.g. retransmission
Error correction: Correct bit errors if possible
Flow control: avoid sender outrunning the receiver.
Media access: controlling which frame should be sent over the link next
  Easy for point-to-point links
    Half versus full duplex
  Harder for multi-access links
    Who gets to send?
Switching: How to send frames to the eventual destination?

## Slide 14: Framing
Preamble Postamble
A link layer function, defining which bits have which function
Minimal functionality: mark the beginning and end of packets (or frames).
Some techniques:
  frame delimiter characters with character stuffing
  frame delimiter codes with bit stuffing
  synchronous transmission (e.g. SONET) out of band delimiters
Body

## Slide 15: Byte Stuffing
Mark end of frame with special character
  BISYNC uses “ETX”
  What happens when the user sends this character?
    Use escape character when controls appear in data
  Very common on serial lines; old technique
  View frame as a collection of bytes
Body
SYN
SYN
SOH
Header
STX
ETX
CRC

## Slide 16: Byte Counting
An alternative is to include a count of number of bytes
  Next to the start of frame
  E.g. DDCMP
  Corruptions of count field may cause receiver to receive incorrectly
  Include an error-check to help receiver realize this
Body
Header
SYN
SYN
Class
Count
CRC

## Slide 17: Bit Stuffing
Treat frames as a sequence of bits
Mark frames with special bit sequence
  Example, HDLC: 01111110 is a special sequence or “flag”
    Used at the beginning and end of frame
  But, must ensure data containing this sequence can be transmitted
    Flag can cross byte boundaries
  transmitter inserts a 0 when this is likely to appear in the data:
    111111 -> 1111101
    must stuff a zero any time five 1s appear:
  receiver unstuffs.
Problem with stuffing techniques: frame size depends on data
  Frames can be of different size
  Could lead to some inefficiencies
Body
Header
CRC
Beginning
Sequence
Ending
Sequence