## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3: The ARMv8 Instruction Set
A subset, called LEGv8, used as the example throughout the book
Commercialized by ARM Holdings (www.arm.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See ARM Reference Data tear-out card

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
ADD a, b, c // a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 5: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled LEGv8 code:
ADD t0, g, h // temp t0 = g + h ADD t1, i, j // temp t1 = i + j ADD f, t0, t1 // f = t0 - t1

## Slide 6: Register Operands
Arithmetic instructions use register operands
LEGv8 has a 32 × 64-bit register file
  Use for frequently accessed data
  64-bit data is called a “doubleword”
    31 x 64-bit general purpose registers X0 to X30
  32-bit data called a “word”
    31 x 32-bit general purpose sub-registers W0 to W30
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware

## Slide 7: LEGv8 Registers
X0 – X7: procedure arguments/results
X8: indirect result location register
X9 – X15: temporaries
X16 – X17 (IP0 – IP1): may be used by linker as a scratch register, other times as temporary register
X18: platform register for platform independent code; otherwise a temporary register
X19 – X27: saved
X28 (SP): stack pointer
X29 (FP): frame pointer
X30 (LR): link register (return address)
XZR (register 31): the constant value 0

## Slide 8: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in X19, X20, …, X23
Compiled LEGv8 code:
ADD X9, X20, X21 ADD X10, X22, X23 SUB X19, X9, X10

## Slide 9: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
LEGv8 does not require words to be aligned in memory, except for instructions and the stack

## Slide 10: Memory Operand Example
C code:
A[12] = h + A[8];
  h in X21, base address of A in X22
Compiled LEGv8 code:
  Index 8 requires offset of 64
LDUR X9,[X22,#64] // U for “unscaled”
ADD X9,X21,X9
STUR X9,[X22,#96]

## Slide 11: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 12: Immediate Operands
Constant data specified in an instruction
ADDI X22, X22, #4
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 13: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 14: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 15: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 16: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 0010two
  –2 = 1111 1111 … 1101two + 1 = 1111 1111 … 1110two

## Slide 17: Sign Extension
Representing a number using more bits
  Preserve the numeric value
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In LEGv8 instruction set
  LDURSB: sign-extend loaded byte
  LDURB: zero-extend loaded byte

## Slide 18: Representing Instructions
Instructions are encoded in binary
  Called machine code
LEGv8 instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
§2.5 Representing Instructions in the Computer

## Slide 19: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 20: LEGv8 R-format Instructions
Instruction fields
  opcode: operation code
  Rm: the second register source operand
  shamt: shift amount (00000 for now)
  Rn: the first register source operand
  Rd: the register destination
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits

## Slide 21: R-format Example
ADD X9,X20,X21
1112ten
21ten
0ten
20ten
9ten
10001011000two
10101two
000000two
10100two
01001two
1000 1011 0001 0101 0000 0010 1000 1001two =
8B15028916
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits

## Slide 22: LEGv8 D-format Instructions
Load/store instructions
  Rn: base register
  address: constant offset from contents of base register (+/- 32 doublewords)
  Rt: destination (load) or source (store) register number
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
opcode
op2
Rn
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
address

## Slide 23: LEGv8 I-format Instructions
Immediate instructions
  Rn: source register
  Rd: destination register
Immediate field is zero-extended
opcode
Rn
Rd
10 bits
12 bits
5 bits
5 bits
immediate

## Slide 24: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 25: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | LEGv8
Shift left | << | << | LSL
Shift right | >> | >>> | LSR
Bit-by-bit AND | & | & | AND, ANDI
Bit-by-bit OR | ¦ | ¦ | OR, ORI
Bit-by-bit NOT | ~ | ~ | EOR, EORI
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 26: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  LSL by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  LSR by i bits divides by 2i (unsigned only)
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits

## Slide 27: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
AND X9,X10,X11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
X10
X11
X9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00001100 00000000

## Slide 28: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
OR X9,X10,X11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
X10
X11
X9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00111101 11000000

## Slide 29: EOR Operations
Differencing operation
  Set some bits to 1, leave others unchanged
EOR X9,X10,X12 // NOT operation
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
X10
X12
X9
11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
11111111 11111111 11111111 11111111 11111111 11111111 11110010 00111111

## Slide 30: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
CBZ register, L1
  if (register == 0) branch to instruction labeled L1;
CBNZ register, L1
  if (register != 0) branch to instruction labeled L1;
B L1
  branch unconditionally to instruction labeled L1;
§2.7 Instructions for Making Decisions

## Slide 31: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in X22, X23, …
Compiled LEGv8 code:
SUB X9,X22,X23
CBNZ X9,Else
ADD X19,X20,X21
B Exit Else: SUB X9,X22,x23 Exit: …
Assembler calculates addresses

## Slide 32: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in x22, k in x24, address of save in x25
Compiled LEGv8 code:
Loop: LSL X10,X22,#3 ADD X10,X10,X25 LDUR X9,[X10,#0] SUB X11,X9,X24 CBNZ X11,Exit
ADDI X22,X22,#1 B Loop Exit: …

## Slide 33: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 34: More Conditional Operations
Condition codes, set from arithmetic instruction with S-suffix (ADDS, ADDIS, ANDS, ANDIS, SUBS, SUBIS)
  negative (N): result had 1 in MSB
  zero (Z): result was 0
  overlow (V): result overflowed
  carry (C): result had carryout from MSB
Use subtract to set flags, then conditionally branch:
  B.EQ
  B.NE
  B.LT (less than, signed), B.LO (less than, unsigned)
  B.LE (less than or equal, signed), B.LS (less than or equal, unsigned)
  B.GT (greater than, signed), B.HI (greater than, unsigned)
  B.GE (greater than or equal, signed),
  B.HS (greater than or equal, unsigned)

## Slide 35: Conditional Example
if (a > b) a += 1;
  a in X22, b in X23
  SUBS X9,X22,X23 // use subtract to make comparison
  B.LTE Exit // conditional branch
  ADDI X22,X22,#1
  Exit:

## Slide 36: Signed vs. Unsigned
Signed comparison
Unsigned comparison
Example
  X22 = 1111 1111 1111 1111 1111 1111 1111 1111
  X23 = 0000 0000 0000 0000 0000 0000 0000 0001
  X22 < X23 # signed
    –1 < +1
  X22 > X23 # unsigned
    +4,294,967,295 > +1

## Slide 37: Procedure Calling
Steps required
  Place parameters in registers X0 to X7
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call (address in X30)
§2.8 Supporting Procedures in Computer Hardware

## Slide 38: Procedure Call Instructions
Procedure call: jump and link
BL ProcedureLabel
  Address of following instruction put in X30
  Jumps to target address
Procedure return: jump register
BR LR
  Copies LR to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 39: Leaf Procedure Example
C code:
long long int leaf_example (long long int g, long long int h, long long int i, long long int j) { long long int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in X0, …, X3
  f in X19 (hence, need to save $s0 on stack)

## Slide 40: Leaf Procedure Example
LEGv8 code:
leaf_example:
SUBI SP,SP,#24
STUR X10,[SP,#16]
STUR X9,[SP,#8]
STUR X19,[SP,#0]
ADD X9,X0,X1
ADD X10,X2,X3
SUB X19,X9,X10
ADD X0,X19,XZR
LDUR X10,[SP,#16]
LDUR X9,[SP,#8]
LDUR X19,[SP,#0]
ADDI SP,SP,#24
BR LR
Save X10, X9, X19 on stack
X9 = g + h
X10 = i + j
f = X9 – X10
copy f to return register
Resore X10, X9, X19 from stack
Return to caller

## Slide 41: Local Data on the Stack

## Slide 42: Register Usage
X9 to X17: temporary registers
  Not preserved by the callee
X19 to X28: saved registers
  If used, the callee saves and restores them

## Slide 43: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 44: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in X0
  Result in X1

## Slide 45: Leaf Procedure Example
LEGv8 code:
fact:
SUBI SP,SP,#16
STUR LR,[SP,#8]
STUR X0,[SP,#0]
SUBIS XZR,X0,#1
B.GE L1
ADDI X1,XZR,#1
ADDI SP,SP,#16
BR LR
L1: SUBI X0,X0,#1
BL fact
LDUR X0,[SP,#0]
LDUR LR,[SP,#8]
ADDI SP,SP,#16
MUL X1,X0,X1
BR LR
Save return address and n on stack
compare n and 1
Else, set return value to 1
n = n - 1
if n >= 1, go to L1
call fact(n-1)
Pop stack, don’t bother restoring values
Return
Restore caller’s n
Restore caller’s return address
Pop stack
return n * fact(n-1)
return

## Slide 46: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 47: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People

## Slide 48: Byte/Halfword Operations
LEGv8 byte/halfword load/store
  Load byte:
    LDURB Rt, [Rn, offset]
    Sign extend to 32 bits in rt
  Store byte:
    STURB Rt, [Rn, offset]
    Store just rightmost byte
  Load halfword:
    LDURH Rt, [Rn, offset]
    Sign extend to 32 bits in rt
  Store halfword:
    STURH Rt, [Rn, offset]
    Store just rightmost halfword

## Slide 49: String Copy Example
C code:
  Null-terminated string
void strcpy (char x[], char y[]) { size_t i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }

## Slide 50: String Copy Example
LEGv8 code:
strcpy: SUBI SP,SP,8 // push X19
STUR X19,[SP,#0] ADD X19,XZR,XZR // i=0 L1: ADD X10,X19,X1 // X10 = addr of y[i] LDURB X11,[X10,#0] // X11 = y[i] ADD X12,X19,X0 // X12 = addr of x[i] STURB X11,[X12,#0] // x[i] = y[i] CBZ X11,L2 // if y[i] == 0 then exit ADDI X19,X19,#1 // i = i + 1 B L1 // next iteration of loop L2: LDUR X19,[SP,#0] // restore saved $s0 ADDI SP,SP,8 // pop 1 item from stack BR LR // and return

## Slide 51: 32-bit Constants
Most constants are small
  12-bit immediate is sufficient
For the occasional 32-bit constant
MOVZ: move wide with zeros
MOVK: move with with keep
Use with flexible second operand (shift)
0000 0000 0000 0000
MOVZ X9,255,LSL 16
§2.10 LEGv8 Addressing for 32-Bit Immediates and Addresses
MOVK X9,255,LSL 0
0000 0000 0000 0000
0000 0000 1111 1111
0000 0000 0000 0000
0000 0000 0000 0000
0000 0000 0000 0000
0000 0000 1111 1111
0000 0000 1111 1111

## Slide 52: Branch Addressing
B-type
  B 1000 // go to location 10000ten
CB-type
  CBNZ X19, Exit // go to Exit if X19 != 0
Both addresses are PC-relative
  Address = PC + offset (from instruction)
5
10000ten
6 bits
26 bits
181
Exit
8 bits
19 bits
19
5 bits

## Slide 53: LEGv8 Addressing Summary

## Slide 54: LEGv8 Encoding Summary

## Slide 55: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization

## Slide 56: Synchronization in LEGv8
Load exclusive register: LDXR
Store exclusive register: STXR
To use:
  Execute LDXR then STXR with same address
  If there is an intervening change to the address, store fails (communicated with additional output register)
  Only use register instruction in between

## Slide 57: Synchronization in LEGv8
Example 1: atomic swap (to test/set lock variable)
  again: LDXR X10,[X20,#0]
  STXR X23,X9,[X20] // X9 = status
  CBNZ X9, again
  ADD X23,XZR,X10 // X23 = loaded value
Example 2: lock
  ADDI X11,XZR,#1 // copy locked value
  again: LDXR X10,[X20,#0] // read lock
  CBNZ X10, again // check if it is 0 yet
  STXR X11, X9, [X20] // attempt to store
  BNEZ X9,again // branch if fails
  Unlock:
  STUR XZR, [X20,#0] // free lock

## Slide 58: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 59: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 60: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 61: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including SP, FP)
  6. Jump to startup routine
    Copies arguments to X0, … and calls main
    When main returns, do exit syscall

## Slide 62: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 63: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code

## Slide 64: Starting Java Applications
Simple portable instruction set for the JVM
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine

## Slide 65: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(long long int v[], long long int k) { long long int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in X0, k in X1, temp in X9
§2.13 A C Sort Example to Put It All Together

## Slide 66: The Procedure Swap
swap: LSL X10,X1,#3 // X10 = k * 8
ADD X10,X0,X10 // X10 = address of v[k]
LDUR X9,[X10,#0] // X9 = v[k]
LDUR X11,[X10,#8] // X11 = v[k+1]
STUR X11,[X10,#0] // v[k] = X11 (v[k+1])
STUR X9,[X10,#8] // v[k+1] = X9 (v[k])
BR LR // return to calling routine

## Slide 67: The Sort Procedure in C
Non-leaf (calls swap)
  void sort (long long int v[], size_t n)
  {
  size_t i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in X0, n in X1, i in X19, j in X20

## Slide 68: The Outer Loop
Skeleton of outer loop:
  for (i = 0; i <n; i += 1) {
MOV X19,XZR // i = 0
for1tst:
CMP X19, X1 // compare X19 to X1 (i to n)
B.GE exit1 // go to exit1 if X19 ≥ X1 (i≥n)
(body of outer for-loop)
ADDI X19,X19,#1 // i += 1
B for1tst // branch to test of outer loop
exit1:

## Slide 69: The Inner Loop
Skeleton of inner loop:
  for (j = i − 1; j >= 0 && v[j] > v[j + 1]; j − = 1) {
SUBI X20, X19, #1 // j = i - 1
for2tst: CMP X20,XZR // compare X20 to 0 (j to 0)
B.LT exit2 // go to exit2 if X20 < 0 (j < 0)
LSL X10, X20, #3 // reg X10 = j * 8
ADD X11, X0, X10 // reg X11 = v + (j * 8)
LDUR X12, [X11,#0] // reg X12 = v[j]
LDUR X13, [X11,#8] // reg X13 = v[j + 1]
CMP X12, X13 // compare X12 to X13
B.LE exit2 // go to exit2 if X12 ≤ X13
MOV X0, X21 // first swap parameter is v
MOV X1, X20 // second swap parameter is j
BL swap // call swap
SUBI X20, X20, #1 // j –= 1
B for2tst // branch to test of inner loop
exit2:

## Slide 70: Preserving Registers
Preserve saved registers:
SUBI SP,SP,#40 // make room on stack for 5 regs
STUR LR,[SP,#32] // save LR on stack
STUR X22,[SP,#24] // save X22 on stack
STUR X21,[SP,#16] // save X21 on stack
STUR X20,[SP,#8] // save X20 on stack
STUR X19,[SP,#0] // save X19 on stack
MOV X21, X0 // copy parameter X0 into X21
MOV X22, X1 // copy parameter X1 into X22
Restore saved registers:
exit1: LDUR X19, [SP,#0] // restore X19 from stack
LDUR X20, [SP,#8] // restore X20 from stack
LDUR X21,[SP,#16] // restore X21 from stack
LDUR X22,[SP,#24] // restore X22 from stack
LDUR X30,[SP,#32] // restore LR from stack
SUBI SP,SP,#40 // restore stack pointer

## Slide 71: Effect of Compiler Optimization
Chart: 
| none | O1 | O2 | O3
Relative Performance | 1 | 2.37 | 2.38 | 2.41
Chart: 
| none | O1 | O2 | O3
Clock Cycles | 158615 | 66990 | 66521 | 65747
Chart: 
| none | O1 | O2 | O3
Instruction count | 114938 | 37470 | 39993 | 44993
Chart: 
| none | O1 | O2 | O3
CPI | 1.38 | 1.79 | 1.66 | 1.46
Compiled with gcc for Pentium 4 under Linux

## Slide 72: Effect of Language and Algorithm
Chart: 
| C/none | C/O1 | C/O2 | C/O3 | Java/int | Java/JIT
Bubblesort Relative Performance | 1 | 2.37 | 2.38 | 2.41 | 0.12 | 2.13
Chart: 
| C/none | C/O1 | C/O2 | C/O3 | Java/int | Java/JIT
Quicksort Relative Performance | 1 | 1.5 | 1.5 | 1.91 | 0.05 | 0.29
Chart: 
| C/none | C/O1 | C/O2 | C/O3 | Java/int | Java/JIT
Quicksort vs. Bubblesort Speedup | 2468 | 1562 | 1555 | 1955 | 1050 | 338

## Slide 73: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 74: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 75: Example: Clearing an Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
MOV X9,XZR // i = 0 loop1: LSL X10,X9,#3 // X10 = i * 8 ADD X11,X0,X10 // X11 = address // of array[i] STUR XZR,[X11,#0] // array[i] = 0 ADDI X9,X9,#1 // i = i + 1 CMP X9,X1 // compare i to // size B.LT loop1 // if (i < size) // go to loop1 | MOV X9,X0 // p = address of // array[0] LSL X10,X1,#3 // X10 = size * 8 ADD X11,X0,X10 // X11 = address // of array[size] loop2: STUR XZR,0[X9,#0] // Memory[p] = 0 ADDI X9,X9,#8 // p = p + 8 CMP X9,X11 // compare p to < // &array[size] B.LT loop2 // if (p < // &array[size]) // go to loop2

## Slide 76: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer

## Slide 77: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped

## Slide 78: Instruction Encoding

## Slide 79: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions

## Slide 80: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions

## Slide 81: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success

## Slide 82: Basic x86 Registers

## Slide 83: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 84: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 85: Implementing IA-32
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions

## Slide 86: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.19 Fallacies and Pitfalls

## Slide 87: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 88: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 89: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
LEGv8: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks

## Slide 90: Concluding Remarks
Additional ARMv8 features:
  Flexible second operand
  Additional addressing modes
  Conditional instructions (e.g. CSET, CINC)